## Slide 1
STASYS Firmware
FreeRTOS on ESP32 — Dual-Task Architecture for Real-Time Sensor Streaming
Hardware: ESP32 DEVKITV1 + MPU6050 + QMC5883P + Piezo Sensor
Data Rate: 100 Hz Bluetooth packet stream (1 kHz internal sampling)
Tasks: sensorTask (Core 1) + batteryMonitorTask (Core 0)
Protocol: SHA-256 challenge-response auth, 36-byte binary packets

## Slide 2
Project Overview
⚙ System Architecture
📦 MCU
ESP32 DEVKITV1 @ 240 MHz — Dual-core Xtensa LX6
📡 IMU
MPU6050 — 3-axis accel (4G) + 3-axis gyro (500 dps)
⛽ Magnetometer
QMC5883P — ±30 Gauss, 16-bit, continuous mode
🔊 Piezo
ADC1_CH7 (GPIO35) — Impact / trigger-sound detection
🔋 Battery
Li-Ion 3.7V + TP4056 — Voltage divider -> GPIO39 (ADC)
⚙️ Transport
Bluetooth Classic SPP — 115200 baud, 36-byte binary packets
🚀 Why FreeRTOS?
▸ Deterministic task scheduling for real-time sensor sampling
▸ Dual-core affinity pins tasks to specific CPU cores
▸ Lightweight tasks with dedicated stacks (4096 / 2048 bytes)
▸ Cooperative + pre-emptive scheduling (priority-based)
▸ Shared memory via volatile globals across task boundary
▸ vTaskDelay for precise timing without busy-waiting
▸ Native Arduino-ESP32 integration — no extra SDK needed

## Slide 3
FreeRTOS Task Architecture
① Core 0 (Bluetooth + Power)
batteryMonitorTask
Stack: 2048 bytes | Priority: 1
• Polls ADC every 2 s
• Voltage -> percentage conversion
• Updates shared volatile batteryPercentage
• Only propagates when delta >= 2%
② Core 1 (Sensor + Bluetooth TX)
sensorTask
Stack: 4096 bytes | Priority: 1
• I2C burst reads at 1 kHz (10x oversampling)
• Peak accel / peak piezo extraction
• Average gyro for clean trace
• Mag read once per 10 ms packet
• Challenge-response auth flow
• XOR checksum packet assembly
• Transmits 36-byte DataPacket over BT SPP

## Slide 4
FreeRTOS Task Creation & Configuration
Task Creation (setup function)
xTaskCreatePinnedToCore( // Sensor task on Core 1
"sensorTask", /* task name */
4096, /* stack words (bytes / 4) */
NULL, /* parameter */
1, /* priority */
NULL, /* handle (unused) */
1); /* pin to Core 1 */
xTaskCreatePinnedToCore( // Battery task on Core 0
"BatMonitor", /* task name */
2048, /* stack size */
NULL, /* parameter */
1, /* priority */
NULL, /* handle */
0); /* pin to Core 0 */
Key Parameters Explained
▸ Task Name
Debug/RTOS trace identifier
▸ Stack Size
Heap words allocated per task
▸ Priority
0 = lowest; higher = preempts lower
▸ Core ID
0 = Core 0, 1 = Core 1 (affinity)
⏱ Timing Configuration Constants
SEND_RATE_MS = 10 — Packet send interval (100 Hz output rate)
OVERSAMPLE_LOOPS = 10 — I2C + ADC reads per packet (1 kHz internal)
CPU_FREQ_MHZ = 240 — ESP32 max clock speed for timing precision
Stack (sensorTask) = 4096 bytes — Sufficient for I2C buffers + packet assembly
Stack (batteryMonitorTask) = 2048 bytes — Minimal: only ADC read + math

## Slide 5
sensorTask — The 1 kHz Sampling Loop
Loop Flow (every 10 ms)
1. Auth Check
2. 1 kHz Oversampling Loop
3. Magnetometer Read
4. Packet Assembly
5. XOR Checksum
6. BT Transmission
📊 Key RTOS Techniques
Peak Extraction
jerk-based shock detection in oversampling window
Gyro Averaging
Sum/10 smooths high-frequency noise for stable trace
Volatile Shared State
isAuthenticated, batteryPercentage safely read across task boundary
Blocking BT Write
SerialBT.write() blocks → naturally enforces 100 Hz output rate
Pin-to-Core
pinned to Core 1 avoids contention with BT stack on Core 0

## Slide 6
batteryMonitorTask — Core 0 Background Task
Implementation
void batteryMonitorTask(void *parameter) {
int lastReportedVal = -1;
for (;;) {
float v = readBatteryVoltage(); // 16-sample ADC avg
int pct = calculateBatteryPercentage(v); // linear scale
if (lastReportedVal == -1 ||
abs(pct - lastReportedVal) >= 2) {
batteryPercentage = pct; // volatile write
lastReportedVal = pct;
}
vTaskDelay(2000 / portTICK_PERIOD_MS); // 2 s period
}
}
FreeRTOS Design Points
Infinite For-Loop
Standard FreeRTOS task pattern — tasks never return
vTaskDelay()
Yields CPU for 2 s; no busy-wait; Core 0 idle otherwise
Shared Volatile
batteryPercentage is volatile int — safe cross-task read
Delta Threshold
Only updates when change >= 2% — reduces unnecessary writes
Core Affinity
Running on Core 0 leaves Core 1 free for sensor I/O
No Locks Needed
Single writer / single reader, uint8 stores are atomic on ESP32

## Slide 7
Inter-Task Synchronization
Shared Variables
volatile bool isAuthenticated
Written by sensorTask after auth; read by sensorTask loop condition
volatile int batteryPercentage
Written by batteryMonitorTask (Core 0); read by sensorTask (Core 1)
volatile bool hmc_present
Set once in setup(); read by sensorTask to decide mag inclusion
Synchronization Patterns Used
Volatile Keyword
All shared state declared volatile. Prevents compiler from caching values in registers across task boundaries.
Atomic Writes
uint8 (battery) and bool (auth) writes are atomic on ESP32 (32-bit ARM). No mutex needed for single-byte stores.
No Mutex / Semaphore
Simplicity tradeoff: each variable has one writer. No deadlock risk, no priority inversion. Acceptable for this use case.
Single-Writer Rule
Each shared variable has exactly one producing task. sensorTask never writes batteryPercentage; batteryMonitorTask never reads sensors.
Blocking BT Write as Signal
SerialBT.write() blocks ~0.36 ms at 115200 baud. This natural pause enforces the 100 Hz cadence without explicit timers.

## Slide 8
Timing Diagram — 10 ms Packet Cycle
▸ Oversampling Loop (1 kHz) — One Iteration = ~1 ms
I2C Read
ADC Piezo
Jerk Calc
Peak Check
Gyro Accum
Delay 400µs
I2C Read
ADC Piezo
… (x10)
Mag Read
BT Send
Next 10 ms cycle...
⏱ Timing Breakdown (per oversampling iteration)
I2C Burst Read
~0.4 ms 14 bytes @ 400 kHz
ADC Read
~0.1 ms 12-bit, 11 dB attenuation
Math (jerk, comparisons)
< 5 µs ARM FPU integer ops
delayMicroseconds(400)
400 µs Fills remaining time to ~1 ms
Total per iteration
~900 µs Leaves margin for jitter
10 iterations
~9 ms Fits within 10 ms SEND_RATE_MS
DataPacket Composition
▸ header[2] 0xAA 0xBB
▸ ax, ay, az (3x float) peak accel m/s²
▸ gx, gy, gz (3x float) avg gyro rad/s
▸ mag_x, mag_y, mag_z (3x int16) raw QMC5883P LSB
▸ piezo (uint16) peak ADC value
▸ battery (uint8) percentage 0-100
▸ checksum (uint8) XOR of payload bytes

## Slide 9
FreeRTOS Concepts Applied
Task
An infinite loop that runs independently. Both sensorTask and batteryMonitorTask are FreeRTOS tasks created with xTaskCreatePinnedToCore().
Core Affinity
Tasks are pinned to a specific CPU core (0 or 1). sensorTask runs on Core 1 to avoid Bluetooth stack contention on Core 0.
Stack
Each task gets its own call stack. sensorTask uses 4096 bytes (deeper due to I2C buffers, SHA-256 context), batteryMonitorTask uses 2048 bytes (lighter).
Priority
Both tasks run at priority 1. Equal priority on different cores means they execute truly in parallel. If on same core, round-robin.
vTaskDelay()
Yields the CPU for a specified time. Used in batteryMonitorTask (2 s) and sensorTask (400 µs inside loop). The task is removed from ready list during delay.
Volatile
Keyword telling compiler not to cache shared variables in registers. Essential for isAuthenticated and batteryPercentage which are accessed by multiple tasks.

## Slide 10
Summary
Design Outcomes
Architecture
Two FreeRTOS tasks on two CPU cores, communicating via volatile shared memory
Real-Time Guarantee
1 kHz oversampling with deterministic timing via delayMicroseconds + vTaskDelay
Resource Efficiency
Minimal stack usage (6 KB total), no mutexes, no dynamic allocation in hot path
Scalability
Task-based design makes it easy to add new sensors or processing stages
FreeRTOS APIs & Patterns
Key FreeRTOS APIs Used
xTaskCreatePinnedToCore() — create task with core affinity
vTaskDelay() — time-based task yield
volatile keyword — cross-task variable safety
Infinite for(;;) loops — standard RTOS task pattern
STASYS — ESP32 FreeRTOS Firmware | 2 tasks | 2 cores | 100 Hz streaming